## Slide 1: SMART INDIA HACKATHON 2026
SurakshaMesh — Low-Cost Wireless Surface Mesh for Real-Time Mine Subsidence Early Warning
Problem Statement ID: SIH26025
Problem Statement Title: Development of an AI-enabled Low Cost Real Time Mine Subsidence Monitoring, Prediction and Early Warning System for Underground Coal Mines in India
Organization: Coal India Limited (CIL) / Ministry of Coal
Theme: Disaster Management
PS Category: Hardware
Team Name: SurakshaMesh (Team DhartiNode)

## Slide 2: IDEA TITLE: SurakshaMesh — Surface Mesh, First Alert
1. Proposed Solution & Architecture
• Autonomous wireless sensor nodes arranged in a surface mesh directly above underground coal extraction panels.
• Edge Sensor Fusion: 6-Axis MEMS IMU (pitch, roll @ 50 Hz) + rolling Vibration RMS + local Active Buzzer & LED alarms.
• Zero-Latency Mesh: ESP-NOW peer-to-peer radio protocol -> Central Gateway -> Real-time Hexagonal Digital Twin Dashboard.
• Working Prototype: 3 physical hardware nodes with auto-tare calibration, multi-node spatial coherence, and scheduled blast filter.
2. How It Solves Coal India's Problem
• Current method: Manual monthly DGPS surveys detect subsidence post-facto (after surface houses & haul roads have cracked).
• SurakshaMesh: Always-on 24/7 continuous micro-movement tracking as a first-alert layer; DGPS remains periodic calibration.
3. Innovation and Uniqueness
• Multi-Node Spatial Coherence: Distinguishes large-scale geological subsidence from single-point vehicle or animal noise.
• Ultra-Low Cost: ₹1,500 benchtop node / ₹6,000–8,000 industrial solar field station vs ₹15+ Lakhs imported surveying gear.
• Offline-First & Blast-Aware: Runs standalone with local audio sirens even if internet dies; includes a 60s scheduled blast mute window.
SurakshaMesh

## Slide 3: TECHNICAL APPROACH & SYSTEM ARCHITECTURE
1. Technologies & Hardware Stack
• Hardware: ESP32 (Xtensa Dual-Core 240MHz), MPU6050 6-DOF IMU, TP4056 + 21700 LiPo (4000mAh, 3.7V) battery, Active Buzzer.
• Firmware: Embedded C/C++ on FreeRTOS, native I2C register driver (400kHz), Complementary Filter (98% Gyro + 2% Accel @ 50Hz).
• Software: Next.js 16 (App Router), React 19, TypeScript, Tailwind CSS, Node.js Serial-to-HTTP Gateway Bridge, Web Audio API.
2. AI & Geotechnical Decision Engine
• Dynamic Ground-Zero Tare: Calibrates initial resting angles to evaluate pure relative ground deflection (ΔPitch, ΔRoll).
• Statistical Baseline Learning: Welford's algorithm accumulates 60 quiet samples to learn the ambient noise floor (mean & std dev).
• Unsupervised Anomaly Detection: Isolation Forest on multi-variate feature vector [ΔPitch, ΔRoll, PitchRate, RollRate, VibRMS, STA/LTA].
• Spatial Coherence Consensus: Confirms active strata sag when 2+ adjacent nodes tilt in the same direction simultaneously.
3. Data Flow Pipeline
• Surface Nodes (50Hz IMU) ──[ESP-NOW Mesh]──> Central Gateway ──[Serial Bridge]──> Dashboard & AI Engine ──> Live 3D Hex Map & Audio Siren
SurakshaMesh

## Slide 4: FEASIBILITY, VIABILITY & RISK MITIGATION
1. Feasibility & Commercial Viability
• 100% COTS Components: Uses commercially available, ruggedized hardware (ESP32, MEMS, Li-ion, sub-GHz radio).
• Live Working 3-Node Prototype: Built and verified with live wireless mesh telemetry, auto-tare calibration, and audio alarms.
• High Cost Feasibility: Field station at ~₹6,000–8,000 -> Entire 8-node panel mesh demo under ₹60,000 (cheaper than 1 manual survey day).
2. Key Challenges & Engineering Solutions
• MEMS Thermal Drift: Temperature swings (15°C–45°C) cause apparent tilt -> Solved via onboard MPU6050 temperature logging.
• Mine Blasting False Alarms: Heavy dynamite shocks -> Solved via 3s persistence filter + One-Click 60s Scheduled Blast Mode.
• Radio Range in Open Mines: 2.4GHz Wi-Fi blocked by spoil heaps -> Transition to Sub-GHz LoRa (SX1278 433/868 MHz) for 2–5 km range.
• Weather & Coal Dust: Ingress risks -> IP65 weather-sealed black box enclosure with rubber gaskets and solar top lid.
SurakshaMesh

## Slide 5: IMPACT, BENEFITS & SOCIAL VALUE
1. Target Audience & Stakeholders
• Coal India Limited (CIL) colliery managers, CMPDI survey teams, Directorate General of Mines Safety (DGMS).
• Communities & infrastructure located above Bord-and-Pillar / Longwall extraction panels (Jharia, Raniganj, Korba coalfields).
2. Key Benefits & Real-World Value
• Life Safety (Social): Early evacuation warning hours-to-days before sudden sinkhole collapse, preventing loss of life.
• Operational Continuity (Economic): Prevents emergency haul road blockages, equipment burial, and multi-crore structural damage.
• Disaster Containment (Environmental): Early detection of surface fissure openings prevents surface water from flooding underground seams and contains spontaneous coal seam fires.
• Aatmanirbhar Bharat (Strategic): Fully indigenous, low-cost hardware and open-source software stack tailored for Indian mines.
SurakshaMesh

## Slide 6: RESEARCH, REFERENCES & FINALE ROADMAP
1. 90-Day Grand Finale Execution Roadmap
• LoRa Sub-GHz Mesh: Transition from ESP-NOW to SX1278 / SX1262 LoRa modules (Slotted TDMA) for 100+ nodes over a 5 km mining panel.
• Solar Deep-Sleep Power: 21700 4000mAh cell + 1.5W solar lid + 10µA deep-sleep -> 3–5+ years maintenance-free operation.
• Crack Extensometers: Spring-loaded draw-wire sensors across surface tension cracks for millimeter-level displacement tracking.
• Predictive AI Modeling: Knothe Time-Factor subsidence bowl model + small LSTM temporal forecast predicting ground sag 24–48 hours ahead.
• Industrial Edge Gateway: Raspberry Pi Gateway with 4G LTE module for offline pit-office GIS maps and emergency SMS broadcasting.
2. Core References & Technical Standards
• Coal India Limited (CIL) SIH26025 Problem Statement Guidelines.
• DGMS Technical Circulars on Ground Control & Subsidence Management in Underground Coal Mines.
• CMPDI Standard Guidelines on Underground Strata & Surface Subsidence Prediction Curves.
• Liu et al., 'Isolation Forest for Unsupervised Anomaly Detection', IEEE ICDM.
• Madgwick / Mahony Sensor Fusion Algorithms for Low-Cost MEMS Attitude & Heading Reference Systems.
SurakshaMesh